## Slide 1
How to Use the
Functions
NEXT
EasyDent V4

## Slide 2
NEXT
Image Effects
Implant
Simulation
Basic Tools
Usage
Divide
a Window

## Slide 3
Image Effects
NEXT
EasyDent V4

## Slide 4
Image Tools
NEXT
Invert
Soft tissue such as blood vessels and nerves that looked dark in the original image will appear with enhanced details.
Sharpen
Increase the contrast of the pixels to enhance the clarity of the image.
Sharpen More
Sharpen 2-3 times more than Sharpen.
Median
Eliminate noise in the image. It filters each pixel data in a way that each pixel takes the median of its surrounding pixels.
Gray Scale
Control brightness in step levels, from white to black.
Coloring
Convert the black and white image into a colored
one. Red signifies high density and blue signifies low
density.
Film Effect
Modify the image, so that it will have the effects of
the texture of developed film.
Rotation
Rotate the image in four different angles.
Local
Enhancement
Highlight a specific area of an image and make it
easier to view.
Zoom In/Out
Zoom in or out on an image.
Move
Move the entire image.
Property
Rotate the image and modify the tooth number.
Adjust
Adjust the brightness, contrast, and gamma values for an image.

## Slide 5
Image Tools - Invert
Click!!
①
NEXT

## Slide 6
Image Tools - Sharpen
Click!!
①
Click!!
③
R-Click!!
②
Normal
Sharpen
NEXT

## Slide 7
Image Tools – Sharpen More
Click!!
①
Click!!
③
R-Click!!
②
Normal
Sharpen
NEXT

## Slide 8
Image Tools – Median
Click!!
①
Click!!
③
R-Click!!
②
Normal
Median
NEXT

## Slide 9
Image Tools – Gray Scale
Click!!
①
Click!!
③
R-Click!!
②
Normal
Gray Scale
NEXT

## Slide 10
Image Tools – Coloring
Click!!
①
Click!!
③
R-Click!!
②
Normal
Coloring
NEXT

## Slide 11
Image Tools – Film Effect
Click!!
①
Click!!
③
R-Click!!
②
Normal
Film Effect
NEXT

## Slide 12
Image Tools – Rotation
Click!!
④
R-Click!!
③
Click!!
①
Click!!
②
NEXT

## Slide 13
Image Tools – Local Enhancement
Click!!
①
NEXT
Click!!
②

## Slide 14
Image Tools – Zoom In/Out
Click!!
①
NEXT

## Slide 15
Image Tools – Move
Click!!
①
NEXT

## Slide 16
Image Tools – Property
Click!!
①
NEXT

## Slide 17
Click!!
①
Image Tools – Adjust
NEXT

## Slide 18
Basic Tools Usage
NEXT
EasyDent V4

## Slide 19
Draw Tool
NEXT
Free Draw
User can draw freely on the image.
Line
User can draw straight lines on the image.
Poly-Line
User can draw continuous lines on the image.
Rectangle
User can draw a rectangle on the image.
Ellipse
User can draw an elliptical shape on the image.
Color
Use can change the color of the line drawn on the image.
Style
User can change the style of lines used on the image using the Drawing Tool.
Delete
User can delete all drawings on the image using the Drawing Tool.

## Slide 20
Free Draw
Click Draw → Free Draw on the menu bar at the top of the EasyDent
Viewer window, or click on the DRAWING icon on the toolbar.
Then, draw freely on the image.
Line
To draw a line, click Draw → Line. Click and hold the mouse at the start
point. Drag and let go of mouse at the end point. Then a line segment appears
between two points.
Poly-Line
To draw a poly-line, click Draw → Poly-Line. Click the mouse
at the start point, followed by clicks at certain points, and then
double-click the mouse at the end point.
Draw Tool

## Slide 21
Rectangle
Click Draw → Rectangle on the menu bar at the top of the main
screen, and then draw any rectangular shape on the image.
Ellipse
Click on Draw → Ellipse, then draw an elliptical shape on the image.
Moving a Poly-Line
The poly-line drawn can be moved to a desired position. To move it,
follow the following steps.
① If a Poly-Line on the image is clicked, using the Select
Button on the toolbar, all the vertexes transform into a square.
② At this stage, click and drag the Poly-Line, to the desired location.
Draw Tool

## Slide 22
Draw Tool
Click!!
Click!!
Change the Color
① Click Draw → Color, then choose colors from Black,
White, Gray, Green, Blue, Yellow, and Red.
② Click User for more different colors other than the above-
mentioned ones. A full color palette will appear.
Change the Line Style
① Click Draw → Style, to change the types of lines used when drawing
on the image.
NEXT

## Slide 23
Draw Tool
Delete All
① Click Draw → Color, choose colors from Black,
White, Gray, Green, Blue, Yellow, and Red.
② Click User for more different colors other than the above-
mentioned ones. A full color palette will appear.
Click!!
NEXT

## Slide 24
Draw Tool
Delete All
① Click Draw → Color, choose colors from Black,
White, Gray, Green, Blue, Yellow, and Red.
② Click User for more different colors other than the above-
mentioned ones. A full color palette will appear.
Click!!
R-Click!!
③
Click!!
NEXT

## Slide 25
Measure Tool
NEXT
Distance
User can draw freely on the image.
Continuous Distance
User can measure the distance between several points, continuously.
Angle
User can measure the angle between two lines on the image.
Delete All
User can delete all measurements on the current image that was created using the Measure Tools.

## Slide 26
Distance
Click Measure → Distance on the menu bar,
or the MEASURE icon on the toolbar.
Measure Tool
Continuous Distance
① Click Measure → Continuous Distance.
② Click the mouse at the start point, followed by clicks at certain points,
and then double-click the mouse at the end point to acquire distance.
Angle
① Click Measure → Angle.
② You may measure any angle on any part of the image.
Click on three separate points to create an angle.
NEXT

## Slide 27
Delete All
Click on Measure → Delete All, all distances and angles added using the measuring tool will be deleted.
Measure Tool
Click!!
NEXT

## Slide 28
Special Tool
NEXT
Magnifier
User can magnify a specific area of an image.
Magnifier LE
Magnifier LE (Local Enhancement) is a combination of the Magnifier and the Local Enhancement tools.
Slide
Patient’s images are shown in the form of a presentation slide.
Profile
User can measure the density of the teeth before an implant placement.
Dual Monitor
This tool is available only if a dual monitor setup is recognized in the operating system.
Whitening
This tool is available if an image was taken by an intraoral camera.
Snapshot
User can capture an image of the screen in 3 forms (Full Screen, Window, and Area).
Crop Image
User can crop an intraoral sensor image.
Layout Editor
This tool provides tools to create a user-defined layout.

## Slide 29
Click!!
①
Special Tool - Magnifier
NEXT

## Slide 30
Click!!
①
Special Tool – Magnifier LE
NEXT

## Slide 31
Click!!
①
Special Tool – Slide
NEXT

## Slide 32
Click!!
①
Special Tool – Profile
NEXT

## Slide 33
Click!!
①
Special Tool – Whitening
NEXT

## Slide 34
Click!!
①
Special Tool – Crop Image
R-Click!!
Click!!
Click!!
Click!!
Click!!
NEXT

## Slide 35
Implant Simulation
NEXT
EasyDent V4

## Slide 36
Implant Simulation
Click!!
①
NEXT
Delete All Implant
Delete All Implant Crown

## Slide 37
Divide a Window
NEXT
EasyDent V4

## Slide 38
Window
NEXT

## Slide 39
Thank you
FAQ