## Slide 1
NEXT
Patient Registration
and Basic Usage Guide
EasyDent V4
Notes: 수진자 정보 관리
이미지 정보 관리
영상정보 내보내기
영상자료 가져오기
CT 영상 가져오기
도움말 EasyDent Viewer 버전 정보 보기, 업데이터 실행,

## Slide 2
Settings
NEXT
Introduction to
EasyDent V4 &
Patient
Registration
Basic Usage
Guide
Print Report
& Send
E-mail

## Slide 3
NEXT
EasyDent V4
Introduction to EasyDent V4
& Patient Registration

## Slide 4
Execute the EasyDent V4 software by double clicking the EasyDent V4 icon.
EasyDent V4
EasyDent4
Viewer
Click x 2!!
NEXT

## Slide 5
NEXT
Main Screen
Patient
Information
Displays patient’s photo and personal information such as
chart number, name, age, and sex.
Menu Bar
All functions are divided and listed as items on the menu bar.
Tool Bar
Icons created for quick usage of common tasks, such as image acquisition and search of patients and images etc.
Thumbnail
(Preview Window)
Displays thumbnails of captured images of the patient.
Function Tap
Allows quick selection of different viewing windows within EasyDent.
Patient List
Displays the list of patients.
Image List
Displays a list of images of the patient.
Today’s Captured List
Displays list of all patients that have had a new image captured and added to their chart within the current work day. If you want to enable this function, click Today Captured List.
Network Status

## Slide 6
Menu Bar
NEXT
Menu Bar
All functions are divided and listed as items on the menu bar.
1
2
3
4
5
6
7
1
File, Edit, View : General Operating Instructions
2
Database : Database Management
3
Draw, Measure, Image : Image Processing
4
Tool : Special Tools
5
Implant : Implant Simulation
6
Window
7
Help : About EasyDent V4 Viewer, Configuration and Intra-Oral Sensor
Settings

## Slide 7
Click the add patient icon. A window for registering a new patient will appear.
New Patient Registration
Click!!
①
Fill in the patient information in the fields and then click the “Add” button to complete patient registration.
Click!!
②
NEXT

## Slide 8
Gender
Select the gender of the patient.
Date of Birth
Select the date of birth of the patient. Able to change the notation order from Settings.
Chart No.*
Enter the chart no. of the doctor.
The date is being registered automatically and you are able to cancel the set date from Settings. (Required)
SSN
Enter the citizen number from assigned country.
E-mail
Enter information of the patient in each section.
First Name*
Enter the First name.
You can change the notation order from Settings. (Required)
Last Name*
Enter the Last name.
You can change the notation order from Settings. (Required)
Address
Enter address information.
Treatment
Select the state of treatment.
Tel / Mobile
Enter telephone information.
NEXT
* Required fields.

## Slide 9
Click!!
①
Click!!
④
Click!!
⑤
After updating patient info., click the “Modify” button to complete the modification.
Modification of Patient Info.
NEXT
Click!!
②
Click!!
③
*administrative login required.

## Slide 10
Patient Search(1/2)
Click!!
①
Click!!
③
Click!!
④
Click!!
②
Click!!
⑤
NEXT

## Slide 11
Patient Search(2/2)
Double Click!!
①
Double-click on Chart No., First Name or Last Name to display virtual keyboard.
NEXT

## Slide 12
Basic Guide
NEXT
EasyDent V4

## Slide 13
② The capture software will be executed.
Image Capture – Extra Oral Equipment(1/2)
① Select the Modality from the File tab on the menu bar.
Click to capture for 2D & 3D images.
Click to capture Panoramic image.
Click to capture Cephalometric image.
NEXT
*Panorama & Cephalo are for 2D devices only.
*
*

## Slide 14
① Select the Modality.
Click to capture for 2D & 3D images.
Click to capture Panoramic image.
Click to capture Cephalometric image.
Image Capture – Extra Oral Equipment(2/2)
② The capture software will execute.
Click!!
Click!!
Click!!
NEXT

## Slide 15
Import Image
Click!!
④
Click!!
⑤
Click!!
⑥
Click!!
⑦
Click!!
⑧
Click!!
①
Click!!
③
Click!!
②
NEXT

## Slide 16
Image Transfer
Click!!
①
Click!!
③
Click!!
⑤
Click!!
④
Click!!
⑥
Click!!
⑦
Click!!
⑧
NEXT
Click!!
②
*administrative login required.

## Slide 17
Image Delete
Click!!
①
Click!!
③
Click!!
④
Click!!
⑤
Click!!
⑥
Click!!
⑦
NEXT
Click!!
②
*administrative login required.

## Slide 18
Export Data
Click!!
②
User Setting
The user can specify the storage capacity for
the image(s) to be exported.
Select a patient
Export the most recent images for the selected
patient into an Excel file.
Path
Shows the path where the exported patient data
will be saved.
Click!!
③
Click!!
④
Export Data
Click!!
⑤
NEXT
Click!!
①
*administrative login required.

## Slide 19
Click!!
①
Click!!
②
CD/DVD Burning
① Select mode option from the Select Burn Mode window.
② Insert a blank CD into the drive.
Then the CD Burner window will appear, as shown below. Click the Burn button.
Click!!
③
Click!!
④
NEXT

## Slide 20
Print Report
& Send Email
NEXT
EasyDent V4

## Slide 21
Click!!
①
Click!!
②
① Using patient search, user selects the patient to
create a Report.
Click!!
④
Report Printing(1/2)
Click!!
⑤
Click!!
③
NEXT

## Slide 22
Report Printing(2/2)
Thumbnail
Displays which patient’s images user wants to print.
Preview
Provides a preview of the images and contents that user want to print.
Print Setup
Choose selection and configuration of the printer.
Image Scale
The user can adjust the image scale to 1:1 or fit on screen.
Comment
The user can write in the Title, Header, and Footer.
Date Type
The user can change the date format when printing.
Print
Prints report according to the user's settings.
Cancel
The user can cancel the printing process.
NEXT

## Slide 23
Click!!
①
Click!!
②
Click!!
④
Export to E-mail(1/2)
Click!!
③
NEXT
① Click File  Export to E-mail, a pop-up windows appear
as shown below.
User can use the ‘Export to E-mail’ function only
if ‘Outlook’ is installed and configured on the computer.

## Slide 24
Click!!
①
Click!!
②
NEXT
R-Click!!
③
Click!!
④
① Right-click the mouse and select Export to E-Mail.
Use the ‘Export to E-mail’ function only if ‘Outlook’ is installed and configured on the computer.
Export to E-mail(2/2)

## Slide 25
Settings
NEXT
EasyDent V4

## Slide 26
Click!!
①
Click!!
②
Network Configuration(1/3)
① Click Help  Configuration, a pop-up window appears
as shown below.
Configure the DB Server’s IP address. It consists of
Local Host and Remote Host.
Configure the File Server’s IP Address. It consists of
Local Host and Remote Host.
The Connection Time is the time that the server waits
in order to connect; while the Response Time is the
time taken for the reception of data after the
connection to the server is accomplished. The initial
value for each time is optimized, so we recommend
keeping the initial value, unless otherwise specified.
NEXT

## Slide 27
Click!!
①
Click!!
②
① Click on to the Remote Host section of the DB Server IP Address. Then, input the IP Address of the DB Server computer.
② Click on to the Remote Host section of the File Server IP Address. Then, input the IP
Address of the File Server computer.
③ Click on the ‘Apply’ button.
Click!!
③
When the DB and the File Servers are installed on
separate computers.
NEXT
Network Configuration(2/3)

## Slide 28
③ Click on the ‘Apply’ button.
When the DB and the File Servers are installed on the same computer.
Click!!
②
Click!!
①
① Click on to the Remote Host section of the DB Server IP Address. Then, input the IP Address of the DB Server computer.
② Click on to the Remote Host section of the File Server IP Address. Then, input the IP Address of the File Server computer.
Click!!
③
NEXT
Network Configuration(3/3)

## Slide 29
Drawing
Choose the style of the line (Dotted, Thin, Medium, or Bold) and its color in the
Drawing Tools.
Measure
Select the style (Dotted, Thin, Medium, or Bold) and color of the line to be used in
the ‘Measuring Tools’.
Implant
Choose the color of the Implant.
Drawing
Choose the style of the line (Dotted, Thin, Medium, or Bold) and its color from the
Drawing Tools.
Configuration - Overlay
NEXT

## Slide 30
Configuration - Image Processing
Image Setting
Saves the current Bright, Contrast and Gamma
levels. The default setting is Not in Use.
Another Image
Processing
Sets the current Coloring, Film Effect, Invert and Gray Scale image process.
NEXT

## Slide 31
Configuration - Default
Setting Chart No.
Click ‘Use’ to set the length of the chart number.
Language
Select preferred language.
Linkage.xml
-Birthday
Interface the patient’s information with a third-party program through
Linkage.xml.
Scale of
preview window
Start mode
Dual Monitor
Option to use dual monitors.
Magnifier
Size / Ratio / Color.
Ratio on screen
Choose Intraoral Sensor’s proportion to the screen.
Login Option
Options include ‘Use Login’, ‘Not Use Login’, or ‘Auto Login’ for user when executing EasyDent.
Date & Time
NEXT

## Slide 32
Configuration - Program
Select dental
formula
Choose a dental formula.
Software for
Analysis
Select either EzCeph or OrthoVision, either program can be used for analyzing CEPH images.
Select capture
mode for Dental CT
Choose the capture mode for dental CT Equipment.
Select capture
mode for Panorama
Choose the capture mode for panoramic equipment.
Path for
TOMO Viewer
Path for
CT Viewer
Enable
CR Scanner
NEXT

## Slide 33
Thank you
FAQ